## Slide 1: ALZHEIMER’S VIRTUAL ASSISTANT
Submitted by:
4 BIT CODE

## Slide 2: AGENDA
Executive Summary
Solution Brief
Components used
Implementation details
Circuit implementation
Constraints
About Us

## Slide 3: Executive Summary
Alzheimer's disease is a progressive disorder that causes brain cells to degenerate and die. It is the most common form of dementia. Worldwide, around 50 million people have dementia, and there are nearly 10 million new cases every year. In India, more than 1 million cases are reported per year. This disease is mostly found in persons aged 65 or above. The patients affected by this disease should be treated with utmost care but lack of attention may lead to unexpected deaths.
To tackle these situations and to help the patients and caretakers, we have come with an idea of ALZHEIMER’S VIRTUAL ASSISTANT. This is a wearable device which reminds the patient about the tasks like medications, exercises and other activities. It also alerts caretakers in Emergency situations and will also monitor the patients. In addition to this, we have incorporated health monitoring parameters so that it would be a complete medical aid for the patients.

## Slide 4: Solution Brief
We have designed this system with 2 parts:
  A Wearable device(as in like a watch) for the patients.
  An app for caretakers so that they could monitor the patient parameters through a mobile phone.
Features incorporated in this device:
  Fall detection – It will alert the caretaker through the mobile app when patient falls down.
  Pressure Sensing unit
  Temperature Sensing unit – measures temperature of the patient
  Reminders about medications, exercises and daily activities
  Alert caretakers in emergency situations( patients could alert caretakers themselves in such situations)
  Date and time
  Heart rate sensor and oxygen saturation level monitoring
  Location detection – indicates the live location of the patient

## Slide 5: COMPONENTS USED
HARDWARE COMPONENTS:
  Arduino MKR1000
  Infineon Sensor Hub nano
  HC-05 Bluetooth module
  Nokia 5110 LCD display
  Buzzer and LED
  Heart rate sensor
  Blood oxygen saturation sensor
  Apps and online services
SOFTWARE COMPONENTS:
  Arduino IDE
  Blynk IOT platform

## Slide 6: Implementation Details
This wearable device mainly works on the board Arduino MKR1000 and a Bluetooth module HC-05 is connected with Arduino board to communicate with Infineon’s sensor hub Nano.
The device mainly working on Master-Slave asymmetrical configuration which Arduino board works as master.
This circuitry is connected with Blynk IOT platform so that the device can communicate with caretaker’s smart phone with Blynk app.
Infineon’s sensor hub Nano is used to measure pressure, temperature and altitude.
Configuration is done in two stages
  First stage is Bluetooth module configuration using Arduino board.
  Arduino board configuration.

## Slide 7: CIRCUIT IMPLEMENTATION

## Slide 8: CIRCUIT IMPLEMENTATION
Blynk app screeenshot

## Slide 9: CONSTRAINTS
In this current pandemic situation it was not easy to find hardware kit required for our specification. We couldn’t also find any simulation software for the same so that we are unable to demonstrate it’s working.
Due to time constraint, some of the features that we have mentioned in this project will be implemented in its future developmental stage.

## Slide 10: ABOUT US
Jibi Antony – Team Leader
Electronics and Biomedical Engineering
V Anandhu
Electronics and Biomedical Engineering
Binusree M B
Electronics and Biomedical Engineering
Swathi Krishna M
Electronics and Biomedical Engineering

## Slide 11
THANKYOU